## Slide 1: Flakes, Flights, and Forecasts: Snowpack Measurement Enhancements in the Uinta Mountain Headwaters
MAY 21, 2024
U.S. Bureau of Reclamation
Snow Water Supply Forecasting Program
Colorado River Authority of Utah
Central Utah Water Conservancy District
Utah Division of Water Resources
Lily Bosworth, Rachel Musil
Notes: Mention others attending presentation

## Slide 2
Background

## Slide 3: 5-Year Management Plan & FY24 Work Plan
Drought Mitigation
Measurement
Hydrology & Operations
Flakes, Flights, & Forecasts
Notes: - The Authority adopted a 5-year management plan with three priority areas.
- Measurement, Hydrology and Operations, Drought Mitigation.
- These priorities are in place for 5 years, as described in the Plan, and specific actions are described in the Fiscal Year work plans
The FY 2024 work plan is in progress
The FY 2025 work plan is in development

## Slide 4: Challenge & Need
Conventional snow monitoring misses important dynamics. Improved data is needed to support decision making.
Daniels-Strawberry
Currant Creek
Strawberry Reservoir
Notes: Candice

## Slide 5: Project Objectives
Drought mitigation and resilience
Disseminate results to other watersheds throughout the state
Environmental protection
Optimized flood control operations of federal facilities
Short- and long-term water management decisions
1
2
3
4
5
Notes: Candice

## Slide 6: Airborne Snow Observatories, Inc.
Snow-Free Flight = Lidar
Snow-On Flights = Lidar + Spectrometry
Model Snowpack = iSnobal
Forecast Runoff = WRF-Hydro
Compare = CBRFC, SNOTEL
Operate = SACS
Plan = UCRAF
Experimental
Established
Notes: Beginning at the NASA Jet Propulsion Laboratory 10 years ago, and currently as a Public Benefit Corporation, ASO combines measurements from airborne lidar and spectrometer sensors with physical models of the snowpack and hydrology to produce the best-available snowpack monitoring to support runoff prediction.
Build on the foundation provided by the existing station and manual measurements to capture complete, high-resolution, and high-accuracy measurements of the mountain snowpack to support greater accuracy in runoff forecasting.

## Slide 7: Project Location

## Slide 8: Budget & Timeline
FUNDING SOURCES​ | AMOUNT​
Non-Federal Entities​ | 
1. Colorado River Authority of Utah​ | $ 650,000.00​
2. Central Utah Water Conservancy District​ | $ 250,000.00​
3. Utah Division of Water Resources​ | $ 100,000.00​
Non-Federal Subtotal​ | $1,000,000.00​
Reclamation Federal Funding​ | $ 999,999.00​
TOTAL PROJECT COST​ | $1,999,999.00​
‘24
‘25
‘26
‘27
‘23

## Slide 9: Support

## Slide 10
Year 1
Measurement
& Modeling

## Slide 11
Year 1 Measurement
‘24
10/19
1/16
5/16
4/13
3/19
11
Notes: Per survey, ASO produces 3m and 50m resolution snow depth, 50m SWE, and 50m snow albedo data products – available 3 days post-flight.
These products are provided along with a data report and several graphical and text-based distillations, and are used by our modeling teams to continually track the snowpack state and hydrologic forecasts.
ASO:
Flights to obtain high-resolution snow depth, snow-water equivalent (SWE), and snow albedo mapping
Lidar and imaging spectrometer mapping of mountain snow cover
Seamless, continuous integration with WRF-Hydro and iSnobal
iSnobal is snowpack energy balance model which uses ASO snow depth measurements and produces a snow density map at 50m resolution, the provides a SWE map and then melt rates (see Proposal pg 5)
WRF-Hydro = Weather Research and Forecasting Hydrological modeling system
WRF-Hydro modeling software
Combined with inputs from ASO flights results in real-time weather and hydrologic information including soil moisture, snowpack, shallow groundwater, evapotranspiration, flood inundation, and streamflow
Provides real-time snowpack and water supply forecastingwater and energy budget accounting and operational forecasting data

## Slide 12
Year 1 Reports
‘24
10/19
1/16
5/16
4/13
3/19
Reports:
Data
iSnobal Modeling
WRF Hydro Forecast Modeling
Available online publicly
12
Notes: Per survey, ASO produces 3m and 50m resolution snow depth, 50m SWE, and 50m snow albedo data products – available 3 days post-flight.
These products are provided along with a data report and several graphical and text-based distillations, and are used by our modeling teams to continually track the snowpack state and hydrologic forecasts.
ASO:
Flights to obtain high-resolution snow depth, snow-water equivalent (SWE), and snow albedo mapping
Lidar and imaging spectrometer mapping of mountain snow cover
Seamless, continuous integration with WRF-Hydro and iSnobal
iSnobal is snowpack energy balance model which uses ASO snow depth measurements and produces a snow density map at 50m resolution, the provides a SWE map and then melt rates (see Proposal pg 5)
WRF-Hydro = Weather Research and Forecasting Hydrological modeling system
WRF-Hydro modeling software
Combined with inputs from ASO flights results in real-time weather and hydrologic information including soil moisture, snowpack, shallow groundwater, evapotranspiration, flood inundation, and streamflow
Provides real-time snowpack and water supply forecastingwater and energy budget accounting and operational forecasting data

## Slide 13
Year 1 Results
13
Notes: Per survey, ASO produces 3m and 50m resolution snow depth, 50m SWE, and 50m snow albedo data products – available 3 days post-flight.
These products are provided along with a data report and several graphical and text-based distillations, and are used by our modeling teams to continually track the snowpack state and hydrologic forecasts.
ASO:
Flights to obtain high-resolution snow depth, snow-water equivalent (SWE), and snow albedo mapping
Lidar and imaging spectrometer mapping of mountain snow cover
Seamless, continuous integration with WRF-Hydro and iSnobal
iSnobal is snowpack energy balance model which uses ASO snow depth measurements and produces a snow density map at 50m resolution, the provides a SWE map and then melt rates (see Proposal pg 5)
WRF-Hydro = Weather Research and Forecasting Hydrological modeling system
WRF-Hydro modeling software
Combined with inputs from ASO flights results in real-time weather and hydrologic information including soil moisture, snowpack, shallow groundwater, evapotranspiration, flood inundation, and streamflow
Provides real-time snowpack and water supply forecastingwater and energy budget accounting and operational forecasting data

## Slide 14
Year 1 Results
14
Notes: Per survey, ASO produces 3m and 50m resolution snow depth, 50m SWE, and 50m snow albedo data products – available 3 days post-flight.
These products are provided along with a data report and several graphical and text-based distillations, and are used by our modeling teams to continually track the snowpack state and hydrologic forecasts.
ASO:
Flights to obtain high-resolution snow depth, snow-water equivalent (SWE), and snow albedo mapping
Lidar and imaging spectrometer mapping of mountain snow cover
Seamless, continuous integration with WRF-Hydro and iSnobal
iSnobal is snowpack energy balance model which uses ASO snow depth measurements and produces a snow density map at 50m resolution, the provides a SWE map and then melt rates (see Proposal pg 5)
WRF-Hydro = Weather Research and Forecasting Hydrological modeling system
WRF-Hydro modeling software
Combined with inputs from ASO flights results in real-time weather and hydrologic information including soil moisture, snowpack, shallow groundwater, evapotranspiration, flood inundation, and streamflow
Provides real-time snowpack and water supply forecastingwater and energy budget accounting and operational forecasting data

## Slide 15
Applications

## Slide 16: Runoff and Reservoir Inflow Forecast
16

## Slide 17
17

## Slide 18: Soldier Creek Dam Inflow Forecast
ASO 50%: 77.78 KAF
CBRFC 50%: 72 KAF
18

## Slide 19: Currant Creek Inflow Forecast
ASO 50%: 11.91 KAF
CBRFC 50%: 21 KAF
19

## Slide 20: West Fork of Duchesne Inflow Forecast
ASO 50%: 29.32 KAF
CBRFC 50%: 20 KAF
20

## Slide 21: Upper Stillwater Inflow Forecast
ASO 50%: 62.37 KAF
CBRFC 50%: 70 KAF
21

## Slide 22: Hydrology Inputs to Operations Models
22

## Slide 23: Strawberry Operations Forecast
23

## Slide 24: Upper Stillwater Operations Forecast
24

## Slide 25
cra.utah.gov
@AuthorityUT
@AmyHaasColoRivr
Defending Every Drop
25

## Slide 26
Density
Snow Depth
QAQC is integral to the ASO production pipeline
Airborne Survey
Process Raw Data
Register Snow-off & Snow-on Data
Calculate & Validate Snow Depth
Bias-correct Modeled Density
Calculate SWE
& Estimate Error
HS In-Situ Station Validation | Mean | SD | Min | Max
With HS=0 | -0.66 cm | 4.22 | -13.0 | 11.9
Without HS=0 | -0.93 cm | 4.98 | -13.0 | 11.9
Structural components enforce accuracy
RMSE 0.02m
Mean = 0.03m SD = 0.06m N = 693
Lidar
Point cloud extract
Line-to-line correct
Terrain filter gridding
Spectrometer
Radiance extract
Surface classify
Line-to-line correction:
full-domain consistent accuracy
Co-registration:
minimizes depth bias
Provides depth uncertainty estimate
Depth validation:
Verifies registration
Model density bias adjust:
Informs density & SWE uncertainty
Notes: The ASO snow depth and SWE calculation pipeline has several critical QA/QC steps built in to ensure accuracy.
- Flightline overlap is leveraged to ensure basin-wide data consistency.
- Registration of the snow-on and snow-free data provides reliable and precise depth retrieval, along with an uncertainty estimate on the 3m snow depths, which is checked against in-situ depth measurements (typically 5cm or better).
- The 3m depth error compresses to a very small number (< 1cm) when aggregated to 50m.
- Modeled snow density is evaluated against in-situ measurements and bias-corrected as needed.
Density bias scenarios are used to evaluate SWE sensitivity to the density distribution and inform SWE uncertainty.
ASO – refining the process over the last 10 years
Water managers in neighboring states
Structural elements to ensure data consistency and accuracy
Technical/scientific integrity
Baseline snow-free flight – minimizes errors
Flight patterns provide 4 unique angles for every location
Validate measurements
Testing forecast improvements

## Slide 27: WRF-Hydro Forecast Integration
NCAR WRF-Hydro group operationally produces ASO-constrained hydrologic forecasts using:
Task C.3: Hydrologic Forecasting
ensemble methods (conditioning, scenarios)
other data integrations
performance assessment methods
Notes: Seamless, continuous integration with WRF-Hydro and iSnobal
iSnobal is snowpack energy balance model which uses ASO snow depth measurements and produces a snow density map at 50m resolution, the provides a SWE map and then melt rates (see Proposal pg 5)
WRF-Hydro = Weather Research and Forecasting Hydrological modeling system
WRF-Hydro modeling software
Combined with inputs from ASO flights results in real-time weather and hydrologic information including soil moisture, snowpack, shallow groundwater, evapotranspiration, flood inundation, and streamflow
Provides real-time snowpack and water supply forecasting water and energy budget accounting and operational forecasting data
State of the art column land surface thermodynamics
Dynamic, hyper-resolution terrestrial overland, sub-surface & channel routing
Multi-spatial framework support
Current configuration using 1km column physics with 250m terrain routing
Plan to enable Targeted, refined forecasts for drought mitigation specifically. More localized/better localized forecasts than cbrfc.
How does the project plan to evaluate improvements in accuracy and reliability of water supply forecast model skill with a limited period of record? How will skill improvement be quantified? – wrf hyrdo measured against CBRFC AND actual runoff. Limited period of record, two comparison points. More years (3) will give us a sense of the range of accuracy. Best time to take action is today. Reminder: what’s novel is applying this to Utah.
Jeff: compare open loop wrf hdro to one with aso. Opportunity for aso to refine cbrfc forecast
In many cases, future weather outcomes, not snowpack initial conditions, remain the largest source of water supply forecast uncertainty. How will this be factored into water supply forecast skill? Our goal is to evaulate one variable in the forecasting equation. The weather variables are outside the scope of this study, even though they are impactful. Hopefully ASO will help us allocate resources to areas with impactful and under-measured areas.
Jeff: all models suffer from uncertainty, snowpack is best predictor of water supply, while weather is greatest source of uncertainty. Ensemble forecasting accounts for a range of scenarios. Ensemble can be conditioned.